# Control & Status Registers of TRB3 Peripherial FPGAs
## Control Registers
0xc0
Bits 3-0	HPA output selection for logic analyser debugging
Bit 4	Debug mode enable
Bit 8	Encoder interval selection
Bit 12	Trigger mode selection – '1' with trigger, '0' triggerless run
Bits 5-7 / Bits 9-11 / Bits 13-31	Reserved

0xc1
Bits 10-0	Pre-Trigger window width
Bits 26-16	Post-Trigger window width
Bit 31	Trigger widow enable
Bits 11-15 / Bits 17-30	Reserved

0xc2
Bits 31-1	Channel 31-1 enable
Bit 0	Reserved

0xc3
Bits 31-0	Channel 63-32 enable

## Status Registers
0x80
Bits 7-0	Readout FSM debug information

0x81
Bits 31-0	Empty signals of channels 31-1 and Reference channel

0x82
Bits 31-0	Empty signals of channels 63-32

0x83
Bits 10-0	Pre-Trigger window width
Bits 26-16	Post-Trigger window width
Bits 15-11 / Bits 31-27	Reserved

0x84
Bits 23-0	Valid trigger number
Bits 31-24	Reserved

0x85
Bits 23-0	Valid timing trigger number
Bits 31-24	Reserved

0x86
Bits 23-0	Valid NOtiming trigger
Bits 31-24	Reserved

0x87
Bits 23-0	Invalid trigger number
Bits 31-24	Reserved

0x88
Bits 23-0	Multi timing trigger number
Bits 31-24	Reserved

0x89
Bits 23-0	Spurious trigger number
Bits 31-24	Reserved

0x8a
Bits 23-0	Wrong readout number – wrong readout because of spurious trigger
Bits 31-24	Reserved

0x8b
Bits 23-0	Spike number
Bits 31-24	Reserved

0x8c
Bits 23-0	Idle time with 10 ns granularity
Bits 31-24	Reserved

0x8d
Bits 23-0	Wait time with 10 ns granularity
Bits 31-24	Reserved

0x8e
Bits 23-0	Total number of empty channels (for each readout process)
Bits 31-24	Reserved